## Slide 1: Ioffe Magnet
Design Criteria
Risa Hocking
Research Engineer
Notes: Maximum character recommendations:
Contact info: 145
Main title: 38
Secondary title: 100
Update all text fields with your relevant information.

## Slide 2: Ioffe Overview
PURPOSE
Generate a magnetic field perpendicular to the walls of the cavity to prevent tritium recombination
  Order of 10 mT magnitude
  Decay as quickly as possible
Provide the cavity for CRES (consequence)
PROTOTYPE DIFFERENCES
Maximum length of 2.5 m

## Slide 3: Spatial envelope (full scale)
1.25 m
5.0 m
35°
0.14 m
XZ View
XY View
Rcavity, inner = 327.0 mm
Rcond, inner = 334.35 mm
Rcond, outer = 338.70 mm
0.48 m

## Slide 4: Spatial envelope (prototype)
2.0 m
35°
0.14 m
XZ View
XY View
Rcavity, inner = 327.0 mm
Rcond, inner = 334.35 mm
Rcond, outer = 338.70 mm
0.48 m
Do you need both cones?
Can we do a 1.25 m section instead so that we can use it to scale up to the full ~5 m size?

## Slide 5: Former material
Initially Al 6061
  Very different CTE than Cu/NbTi cable
Copper-based alloys have similar CTE
What is the impact of the alloying constituents on magnetic susceptibility?
Are they available in a form factor that we need?
Plating needed on inside for cavity?
Cost of material (considering cost of machining)?
Material | Composition | Young’s modulus (GPa) | Yield strength (MPa) | Tensile strength (MPa)
Al 6061 | Mg (0.8-1.2%), Si (0.4-0.8%), Fe (0.7%), Cu (0.15-0.4%), Cr (0.04-0.35%), Zn (0.25%), Ti (0.15%), Mn (0.15%) | 68 | 240 | 290
Copper-silicon (C87500) | Pb (0.09%), Zn (12.0-16.0%), Al (0.5%), Si (3.0-5.0%) | 106 | 165 | 414
Silicon bronze (C87300) | Pb (0.09%), Zn (0.25%), Fe (0.2%), Mn (0.8-1.5%), Si (3.5-4.5%) | 112 | 124 | 310
C18160 | Fe (0.10%), Cr (0.2-1.2%), Si (0.1%), Zr (0.05-0.25%) | 137 | 448-496 | 483-621

## Slide 6: Stiffening of cylindrical segments
13 mm
6.65 mm
ID = 654 mm
OD = 680 mm
Suspension ring thickness = 25 mm
Stiffening ring thickness = 10 mm
Maximum deflection = 37 µm under gravity
Note: calculations performed with Al 6061. Need to redo with new alloy.
Notes: Oakridge had success with >6’ diameter indium seals

## Slide 7: Suspension of cylindrical segments
Rsupport tabs = 410 mm
Rsuspension ring = 365 mm
90°
135°°
Rformer = 340 mm
What is threading through the holes for suspension? Rods? Ropes?
Notes: Oakridge had success with >6’ diameter indium seals

## Slide 8: Stiffening and suspension of cones
Suspension point
Suspension point
Another suspension point?
Stiffening ring?
Is the stiffening ring needed?
Do we need suspension on the cone outside of the cylinder/cone join?

## Slide 9: Joining segments together
Indium seal
Stability under thermal cycling
  Anticipate 3*8 = 24 full thermal cycles from cryo to room temp over lifetime
  ORNL has not had issues with cycling indium seals (testing limited to <20 cycles)
Diffusion of indium in copper-based alloy
  May need vacuum grease
Ensuring alignment for indium
Indium type I superconductor -> Tc ~ 3.4 K, Bc ~ 30 mT
  Not a concern
Thermal stability?
Compatibility with copper-based alloys?
Alignment? (rotational + for seal)
Indium wire
(pre-deformation)
Ioffe former
Reworked suspension/joining rings

## Slide 10: Misc. Fabrication
Roundness of cavity?
Centrifugal casting? Seam welding sheet and hot rolling?
Cost?

## Slide 11: Conductor choice
Cost estimate?
NbTi/Cu
Standard 1.3 mm OD MRI cable, 3.2:1 Cu:SC ratio

## Slide 12: Field requirements
If we change these requirements to some resolution and efficiency for CRES, how do we quickly verify that our design meets requirements?
Azimuthal variation: < 0.1 ppm of background field
  Defining as: (range of |B(φ, fixed r) – Bbackground|) / |Bbackground|
Radial variation: < 1 ppm of background field
  Defining as: |B(fixed φ, r) – Bbackground| / |Bbackground|
background field = (0, 0, 20) mT

## Slide 13: Benchmarking field calculation accuracy
Concern: need ppm level field accuracy
  1ppm of 20mT: ~1e-8T
  Most codes: ~ earth magnetic field (~50uT)
Approaches: FEA and Biot-Savart
  RAT (Biot-Savart)
  COMSOL (FEA)
  Opera (Biot-Savart/FEA)
FEA: very small numerical error budget
  Need very dense mesh
  Need large model space (air boundary)
Biot-Savart
  Easy for straight lines, hard for curvature

## Slide 14: Test case
Simple benchmark: infinitely long straight conductor
  Can calculate this analytically (B=µ0I/(2πr))
  COMSOL 2D FEA (solves for Az)
  Opera: Biot-Savart/FEA
    Opera: different FEA implementation (solves for scalar potential)
  RAT: MLFMM/CUDA
COMSOL:
  R = 15 m background
  ~2M DOF, 20 min to solve
Opera: issues
  Adaptive integral for conductors
  Issues with tolerance setting
Opera 3D: 400m long

## Slide 15: Test case
Good agreement COMSOL 2D and analytic
Opera/RAT: good agreement with some/major tweaks
Extrapolating to COMSOL 3D?

## Slide 16: Basic uniformity estimates
σB (ppm)
Additional correction coils? Slightly different transition geometry?
Adjusting current within individual layers? Unwieldy number of power sources?
Note: asymmetry around φ ~ 0° comes from starting coil near a turn; can be alleviated/become more realistic with adding in leads
<1

## Slide 17: Misc. Magnetic Topics
Can we run this in persistent mode?
Full development of quench protection?
Power source requirements?
Allowed geometric tolerances on conductor placement?